## Slide 1
Arduino PWM
Subtítulo
  Thainan Santos Theodoro
  Universidade Federal de Ouro Preto
  João Monlevade, MG
  E-mail: thainan.theodoro@ufop.edu.br
Notes: Agradecimentos: Orientadores, banca interna e externa;
Leitura do Título;
inerge217

## Slide 2
  O PWM
The Pulse Width Modulation (PWM) is widely used in electronic power to operate converters.
Figure – PWM waveforms
Figure – Typical PWM implementation

## Slide 3
  Arduino PWM: AnalogWrite()
The analogWrite() function on Arduino does not generate a true analog signal, as it lacks a DAC (Digital-to-Analog Converter). Instead, it outputs a PWM (Pulse Width Modulation) signal.
Pins | Timer | Freq.
3, 11 | Timer 2 | 490 Hz
5, 6 | Timer 0 | 980 Hz
9, 10 | Timer 1 | 490 Hz
Table - Arduino Uno, Nano, and Pro Mini.
Internal Functioning of analogWrite():
  Checks if the pin supports PWM.
  Configures the corresponding Timer.
  Adjusts the duty cycle using the OCRnX register.
However, Arduino's PWM operates at fixed frequencies of 490 Hz or 980 Hz. It is unsuitable for power converters.

## Slide 4
  Arduino PWM
PWM can be generated in a microcontroller using the following elements:
  Timer/Counters – Used to track time and define the PWM period.
  Comparison Mechanisms – The counter value is compared against a predefined threshold to determine the duty cycle.
  Interrupt Service Routine (ISR) – Can be used to update the PWM signal dynamically when a timer reaches a specific value.

## Slide 5
  Timer/Counters
The Timer/Counter 1 in microcontrollers typically operate in four main modes:
  Normal Mode
  Clear Timer on Compare Match (CTC) Mode
  Phase Correct PWM Mode
  Phase and Frequency Correct PWM Mode

## Slide 6
  Normal Mode
The timer counts up until it overflows and resets to zero.
No automatic waveform generation.
Often used for time delays with interrupts.
Timer | Bit Resolution | Counting Range
Timer 0 | 8-bit | 0 to 255 (0x00 to 0xFF)
Timer 1 | 16-bit | 0 to 65,535 (0x0000 to 0xFFFF)
Timer 2 | 8-bit | 0 to 255 (0x00 to 0xFF)
Figure – Counter.
Table – Technical Characteristics.

## Slide 7
  Clear Timer on Compare Match (CTC) Mode
In CTC, the timer counts up until it reaches a predefined compare value stored in the OCRnA or ICR1 (depending on mode).
ICR1’
ICR1’’
ICR1’’’

## Slide 8
  Fast PWM Mode
The timer counts from 0 to a predefined TOP value (e.g., ICR1), then resets, generating a sawtooth waveform. For example, the OCR1A sets the duty cycle, and OC1A outputs the PWM signal.
Figure – Fast PWM Mode
COUNT
OC1A
ICR1
OCR1A
200
The updates of ICR1 and OCR1A are made at the BOTTOM of counter.

## Slide 9
  Fast PWM Mode
ICR1
OCRA1’
1600
COUNT
OCRA1
400
900
D variation
OC1A
ICR1
OCRA1’
1600
COUNT
OCRA1
400
Freq. variation
OC1A
400
800

## Slide 10
  Phase Correct PWM Mode
The timer is up/down using predefined TOP value (e.g., ICR1), generating a triangular waveform. For example, the OCR1A sets the duty cycle, and OC1A outputs the PWM signal.
Figure – Phase Correct PWM Mode
COUNT
OC1A
ICR1
OCR1A
200
The updates of ICR1 and OCR1A are made at the TOP of counter.

## Slide 11
  Phase Correct PWM Mode
ICR1
OCRA1’
1600
COUNT
OCRA1
400
900
D variation
1600
OC1A
ICR1
OCRA1’
1600
COUNT
OCRA1
400
TOP (ICR1) variation
800
OC1A

## Slide 12
  Phase and Frequency Correct PWM Mode
The timer is up/down using predefined TOP value (e.g., ICR1), generating a triangular waveform. For example, the OCR1A sets the duty cycle, and OC1A outputs the PWM signal.
Figure – Phase and Frequency Correct PWM Mode
COUNT
OC1A
ICR1
OCR1A
200
The updates of ICR1 and OCR1A are made at the BOTTOM of counter.

## Slide 13
  Phase and Frequency Correct PWM Mode
ICR1
OCRA1’
1600
COUNT
OCRA1
400
900
D Variation
1600
OC1A
ICR1
OCRA1’
1600
COUNT
OC1A
OCRA1
400
TOP (ICR1) variation
800

## Slide 14
  Fast PWM Mode
Set registers
  TCCR1A
  TCCR1B
  TIMSK1
  DDRB
Set values
  ICR1
  OCR1A

## Slide 15
  Fast PWM Mode
Registers TCCR1A and TCCR1B
  Clock Select/prescaler (TCCR1B):
    CS12, CS11, CS10.
  Waveform Generation Mode Bit (TCCR1A and TCCR1B):
    WGM13, WGM12, WGM11, WGM10.
  Inverting and non-inverting, Fast PWM (TCCR1A):
    COM1A1, COM1A0, COM1B1, COM1B0.
Register TIMSK1
  Enable interruptions: overflow / match
Register DDRB

## Slide 16
  Frequency
Bit Masking is a technique used to manipulate specific bits within a register without altering the others.
OC1A
TOP
OCR1A
The timer/counter Frequency is,
The PWM Frequency is,

## Slide 17
  Example
Suppose, you need and .
Choosing as prescaler, .
That way, TOP is,
d

## Slide 18
  Bit masking
Bit Masking is a technique used to manipulate specific bits within a register without altering the others.
REGISTER |= (1 << BIT);
Enable a bit (set to 1)
Keeps the other bits unchanged.
Uses bitwise OR (|=).
REGISTER &=~(1 << BIT);
Disable a bit (set to 0)
Keeps the other bits unchanged.
Uses bitwise AND (&=) and NOT (~).

## Slide 19
  Fast PWM Mode

## Slide 20
  Inverting and non-inverting modes

## Slide 21
  Inverting and non-inverting modes